## Slide 1
Chapter 18
Introduction to Network Layer

## Slide 2: Communication at the network layer

## Slide 3: Packetizing
encapsulating the payload in a network-layer packet at the source and decapsulating the payload from the network-layer packet at the destination.
In other words, one duty of the network layer is to carry a payload from the source to the destination without changing it or using it.
Similar to the service of a carrier such as the postal office

## Slide 4: Routing and Forwarding
Other duties of the network layer are
routing
forwarding

## Slide 5: Forwarding process
Forwarding
value
B Data
Send the packet out of interface 2
B
Data

## Slide 6
PACKET SWITCHING
A router is a switch that creates a connection between an input port and an output port (or a set of output ports

## Slide 7: Datagram Approach
The network layer was designed to provide a connectionless service in which the network-layer protocol treats each packet independently, with each packet having no relationship to any other packet.
The idea was that the network layer is only responsible for delivery of packets from the source to the destination.
In this approach, the packets in a message may or may not travel the same path to their destination.

## Slide 8: A connectionless packet-switched network

## Slide 9: Virtual-Circuit Approach
There is a relationship between all packets belonging to a message.
Before all datagrams in a message can be sent, a virtual connection should be set up to define the path for the datagrams.
After connection setup, the datagrams can all follow the same path.
In this type of service, not only must the packet contain the source and destination addresses, it must also contain a flow label, a virtual circuit identifier that defines the virtual path the packet should follow.

## Slide 10: A virtual-circuit packet-switched network

## Slide 11
Forwarding process in a router when used in a virtual
circuit network

## Slide 12: A to B
Sending request packet in a virtual-circuit network
A
t
o B
A to B
A to B

## Slide 13: Sending acknowledgments in a virtual-circuit network

## Slide 14: Flow of one packet in an established virtual circuit

## Slide 15: NETWORK-LAYER PERFORMANCE
The performance of a network can be measured in terms of delay, throughput, and packet loss. Congestion control is an issue that can improve the performance.

## Slide 16: Delay
The delays in a network can be divided into four types:
transmission delay
propagation delay
processing delay
queuing delay

## Slide 17: Throughput
is defined as the number of bits passing through the point in a second, which is actually the transmission rate of data at that point.
In a path from source to destination, a packet may pass through several links (networks), each with a different transmission rate.
How can we determine the throughput of the whole path?

## Slide 18: Throughput in a path with three links in a series

## Slide 19: A path through the Internet backbone

## Slide 20: Effect of throughput in shared links

## Slide 21: Packet Loss
Another issue that severely affects the performance of communication is the number of packets lost during transmission.
The effect of packet loss on the Internet network layer is that the packet needs to be resent, which in turn may create overflow and cause more packet loss.

## Slide 22: Congestion control
A state occurs in the network layer when the message traffic is so heavy that it slows down network response time.

## Slide 23
Congestion control
Open Loop (Prevention)
Closed Loop (removal)
Retransmission Policy
Window Policy
Acknowledgement Policy
Discarding Policy
Admission Policy
Back Pressure
Choke Packet
Implicit signaling
Explicit signaling

## Slide 24: IPv4 ADDRESSES
The identifier used in the IP layer of the TCP/IP protocol suite to identify the connection of each device to the Internet.
An IPv4 address is a 32-bit address that uniquely and universally defines the connection of a host or a router to the Internet.
The IP address is the address of the connection, not the host or the router.

## Slide 25: Three different notations in IPv4 addressing

## Slide 26: Hierarchy in addressing

## Slide 27: Classful Addressing
The whole address space was divided into five classes (class A, B, C, D, and E)
This scheme is referred to as classful addressing.

## Slide 28: Occupation of the address space in classful addressing

## Slide 29: Network address

## Slide 30
Special IP addresses.
Private IP network is an IP network that is not directly connected to the Internet
Private networks use addresses from the following experimental address ranges (non-routable addresses):
  10.0.0.0 – 10.255.255.255 (16,777,216 hosts)
  172.16.0.0 – 172.31.255.255 (1,048,576 hosts)
  192.168.0.0 – 192.168.255.255 (65,536 hosts)

## Slide 31: Subnetting
Subnetting
University Network
Medical
School
Library
Engineering
School
Problem: Organizations have multiple groups/entities within their organization which are independently managed. Each would prefer to manage their own IT facilities, i.e., own network
Solution 1: Allocate to each entity their own IP network/domain
  Organization must own multiple IP address domains
  Expensive (each IP domain costs money) and cumbersome to manage
  Solution 2: Add another level of hierarchy to the existing IP addressing structure

## Slide 32: Basic Idea of Subnetting
Split the host number portion of an IP address into a subnet number and a (smaller) host number.
Result is a 3-layer hierarchy
Then:
    Subnets can be freely assigned within the organization
    Internally, subnets are treated as separate networks
    Subnet structure is not visible outside the organization
network prefix
host number
subnet number
network prefix
host number
extended network prefix

## Slide 33: Typical Addressing Plan for an Organization that uses subnetting

## Slide 34: CIDR - Classless Interdomain Routing
Goals:
  Restructure IP address assignments to increase efficiency
  Hierarchical routing aggregation to minimize route table entries
Key Concept: The length of the network id (prefix) in IP addresses is arbitrary/flexible and is defined by the network hierarchy.
Consequence:
  Routers use the IP address and the length of the prefix for forwarding.
  All advertised IP addresses must include a prefix

## Slide 35: Subnet mask
A class B network subnetted into 64 subnets.
Subnet Mask indicate the split between network + subnet number and host

## Slide 36: Advantages of Subnetting
With subnetting, IP addresses use a N-layer hierarchy. E.g., a 3 layer hierarchy would be:
        Network (IP domain)
        Subnet
        Host
Improves efficiency of IP addresses by not consuming an entire address space for each physical network.
Reduces router complexity. Since external routers do not know about subnetting, the complexity of routing tables at external routers is reduced.
Note: Length of the subnet mask need not be identical at all subnetworks.

## Slide 37: Subnetting Example:

## Slide 38: Network without subnets

## Slide 39: Same Network with Subnets

## Slide 40: Same network with different subnetmasks

## Slide 41
Given an IP address, we can find the subnet address the same way we found the network address. We apply the mask to the address. We can do this in two ways: straight or short-cut.
Finding the Subnet Address
Straight Method
In the straight method, we use binary notation for both the address and the mask and then apply the AND operation to find the subnet address.

## Slide 42
Solution
11001000 00101101 00100010 00111000
11111111 11111111 11110000 00000000
11001000 00101101 00100000 00000000
The subnetwork address is 200.45.32.0.
What is the subnetwork address if the destination address is 200.45.34.56 and the subnet mask is 255.255.240.0?

## Slide 43: CIDR: Prefix Size vs. Host Space
CIDR Block Prefix # of Host Addresses
/27 32 hosts
/26 64 hosts
/25 128 hosts
/24 256 hosts
/23 512 hosts
/22 1,024 hosts
/21 2,048 hosts
/20 4,096 hosts
/19 8,192 hosts
/18 16,384 hosts
/17 32,768 hosts
/16 65,536 hosts
/15 131,072 hosts
/14 262,144 hosts
/13 524,288 hosts

## Slide 44: Example
An organization is granted a block of addresses with the beginning address 14.24.74.0/24. The organization needs to have 3 subblocks of addresses to use in its three subnets: one subblock of 10 addresses, one subblock of 60 addresses, and one subblock of 120 addresses. Design the subblocks.

## Slide 45: ADDRESS AGGREGATION
In Supernetting, multiple networks are combined into a bigger network termed as a Supernetwork or Supernet

## Slide 46
An ISP is granted a block of addresses starting with 190.100.0.0/16 (65,536 addresses). The ISP needs to distribute these addresses to three groups of customers as follows:
a. The first group has 64 customers; each needs 256 addresses.
b. The second group has 128 customers; each needs 128 addresses.
c. The third group has 128 customers; each needs 64 addresses.
Design the subblocks and find out how many addresses are still available after these allocations.
Example 19.10

## Slide 47
Solution
Figure 19.9 shows the situation.
Example 19.10 (continued)
Group 1
For this group, each customer needs 256 addresses. This means that 8 (log2 256) bits are needed to define each host. The prefix length is then 32 − 8 = 24. The addresses are

## Slide 48
Example 19.10 (continued)
Group 2
For this group, each customer needs 128 addresses. This means that 7 (log2 128) bits are needed to define each host. The prefix length is then 32 − 7 = 25. The addresses are

## Slide 49
Example 19.10 (continued)
Group 3
For this group, each customer needs 64 addresses. This means that 6 (log264) bits are needed to each host. The prefix length is then 32 − 6 = 26. The addresses are
Number of granted addresses to the ISP: 65,536
Number of allocated addresses by the ISP: 40,960
Number of available addresses: 24,576

## Slide 50
Figure 19.9 An example of address allocation and distribution by an ISP

## Slide 51: DHCP
address assignment in an organization can be done automatically using the Dynamic Host Configuration Protocol (DHCP).
DHCP is an application-layer program, using the client-server paradigm, that actually helps TCP/IP at the network layer.

## Slide 52: Operation of DHCP

## Slide 53: NAT
A technology that can provide the mapping between the private and universal addresses, and at the same time support virtual private networks
allows a site to use a set of private addresses for internal communication and a set of global Internet addresses (atleast one) for communication with the rest of the world

## Slide 54: Address translation

## Slide 55: Translation

## Slide 56
Position of IPv4 in TCP/IP protocol suite

## Slide 57: The IPv4 (Internet Protocol) header.
Identification
Allow destination host to determine which datagram a newly arrived fragment belongs to. All fragments of a datagram has same id value

## Slide 58: The IP Protocol
Some of the IP options.

## Slide 59: IPv6 - IP Version 6
IP Version 6
  Is the successor to the currently used IPv4
  Specification completed in 1994
  Makes improvements to IPv4 (no revolutionary changes)
One (not the only !) feature of IPv6 is a significant increase in size of the IP address to 128 bits (16 bytes)
IPv6 vs. IPv4: Address Comparison
  IPv4 has a maximum of
      232  4 billion addresses
  IPv6 has a maximum of
    2128 = (232)4  4 billion x 4 billion x 4 billion x 4 billion addresses

## Slide 60: IPv6 Header

## Slide 61: Notation of IPv6 addresses
Convention: The 128-bit IPv6 address is written as eight 16-bit integers (using hexadecimal digits for each integer)
CEDF:BP76:3245:4464:FACE:2E50:3025:DF12
Short notation:
Abbreviations of leading zeroes:
CEDF:BP76:0000:0000:009E:0000:3025:DF12  CEDF:BP76:0:0:9E :0:3025:DF12
“:0000:0000” can be written as “::”
CEDF:BP76:0:0:FACE:0:3025:DF12 
CEDF:BP76::FACE:0:3025:DF12
IPv6 addresses derived from IPv4 addresses have different formats. Convention allows to use IPv4 notation for the last 32 bits.
  128.143.137.144 -> 0:0:0:0:0:ffff:808F:8990

## Slide 62: Extension Headers
IPv6 extension headers.
5-69

## Slide 63: Extension Headers (2)
The hop-by-hop extension header for large datagrams (jumbograms).

## Slide 64: Extension Headers (3)
The extension header for routing.

## Slide 65
Comparison between IPv4 and IPv6 packet headers

## Slide 66: Protocols
ARP
RARP
BOOTP
ICMP

## Slide 67
Address Resolution Protocol(ARP)
  Communication protocol used to discover the data-link layer address(Layer 2 address like Media Access Control(MAC) address) associated with an Internet layer address(Layer 3 address like IPv4 address).
Reverse Address Resolution Protocol
  Allows a newly booted work station to broadcast its ethernet address
  RARP server looksup the Ethernet address in its configuration files and sends back the corresponding IP address
  Since the destn address is all 1s it will not be forwarded by routers, so an RARP server is needed in every network
BOOTP
  Uses UDP messages which are forwarded over routers.
  Provides a diskless workstation with information such as IP address of file server holding memory image, IP address of default router, and subnet mask
  Requires manual configuration

## Slide 68: Internet Control Message Protocol
When something unexpected occurs, the event is reported by ICMP
The principal ICMP message types.
Pkt with DF bit 1, cannot pass through small pkt n/w