## Slide 2: Internet Multicasting
Using Class D addresses
Permanent addresses
  Permanent group exists & need not set up
  224.0.0.1 – all systems on a LAN
  224.0.0.2 – all routers on a LAN
  224.0.0.5 – all OSPF routers on a LAN
  224.0.0.6 – all designated OSPF routers on a LAN
Temporary addresses
  For temporary groups that have to be set before used
  Each host keeps track of which group its processes currently belong to
Implemented by multicast routers & using spanning trees
IGMP – Internet group management Protocol
  Query and Response packet with control information on first word and Class D address on second word

## Slide 6: Multicast Addresses
Local Network control Block -224.0.0.0/24
  224.0.0.1 – all hosts and routers inside a network
  224.0.0.2 – al routers inside a network
Internetwork Control Block
  224.0.1.0/24-multicast to whole internet
Source Specific Multicast (SSM) Block
  232.0.0.0/8 –source specific multicasting
GLOP Block
  233.0.0.0/8 – defines range of addresses to be used inside an AS (233.x.y.0 – 233.x.y.255)
Administratively Scoped Block
  239.0.0.0/8 – used in an particular area of interest, address restricted to an organization

## Slide 8: Delivery at Data Link Layer

## Slide 12
In multicast routing, each involved router needs to construct a shortest path tree for each group.
In the source-based tree approach, each router needs to have one shortest path tree for each group
x

## Slide 13: Group-shared tree approach
In the group-shared tree approach, only the core router, which has a shortest path tree for each group, is involved in multicasting.

## Slide 14: Taxonomy of common multicast protocols
Multicast Open Source Path First
Distance Vector Multicast Routing Protocol
Core Based Trees
Protocol Independent Multicast - Dense Mode
Protocol Independent Multicast – Sparse Mode

## Slide 15
Multicast link state routing uses the source-based tree approach.
Flooding broadcasts packets, but creates loops in the systems.
RPF eliminates the loop in the flooding process.
Reverse path forwarding (RPF)

## Slide 16: Problem with RPF

## Slide 17: RPF Versus RPB
RPB (Reverse Path Broadcasting) creates a shortest path broadcast tree from the source to each destination.
It guarantees that each destination receives one and only one copy of the packet.

## Slide 18: RPF, RPB, and RPM
RPM adds pruning and grafting to RPB to create a multicast shortest path tree that supports dynamic membership changes.

## Slide 19: Group-shared tree with rendezvous router

## Slide 20: Sending a multicast packet to the rendezvous router
In CBT, the source sends the multicast packet (encapsulated in a unicast packet) to the core router.
The core router decapsulates the packet and forwards it to all interested interfaces.

## Slide 21: PIM-DM is used in a dense multicast environment, such as a LAN. PIM-DM uses RPF and pruning and grafting strategies to handle multicasting. However, it is independent of the underlying unicast. PIM-SM is used in a sparse multicast environment such as a WAN. PIM-SM is similar to CBT but uses a simpler procedure.